## Slide 1: Nevada Ave/Tejon St Corridors
June 22, 2022
Todd Frisbie, PE, PTOE,
City Traffic Engineer

## Slide 2
Tejon/Nevada I-25 Interchange Improvements

## Slide 3
PPRTA funded
  Study / Design
  Construction
Goals of the Study
  Identify changes to improve safety for all modes of travel
  Improve traffic flow along S. Nevada
  Encourage southbound I-25 to access Nevada Avenue at the ramp
    Reduce Tejon Street cut-through traffic
Tejon/Nevada I-25 Interchange Improvements
Notes: Provides mobility options for short trips
  Reduces vehicle trips by cars and ride share services
  Reduces congestion
  Complements transit service

## Slide 4
Tejon/Nevada I-25
Crash History

## Slide 5
Tejon/Nevada I-25
Crash Issues

## Slide 6
Tejon/Nevada I-25
Intersection Operations

## Slide 7
The current design has poor operations for vehicles wanting to go from southbound I-25 to southbound Nevada
  There is only a single through lane on the southbound ramp at Tejon (LOS D)
  There is only a shared right-turn lane on southbound ramp at Nevada (LOS E)
Tejon/Brookside and Nevada/Brookside have poor side street operations
Queues often extend through adjacent intersections on Nevada and Tejon
Tejon/Nevada I-25
Intersection Operational Issues

## Slide 8
Travel Patterns – SB I-25
47-55% of Southbound I-25 traffic turning on Tejon is going to Nevada
Vehicles use side streets to get to Nevada:
  Motor Way – 23.9%
  Brookside Street – 10.1%
  Navajo Street – 6.0%
  Ramona Avenue – 1.6%
  St Elmo Avenue – 1.6%
  Cheyenne Road – 9.4%

## Slide 9
Travel Patterns – NB I-25
25% of Northbound I-25 traffic from Nevada uses Tejon as a cut-through
Vehicles use side streets to get to I-25:
  Motor Way – 6.5%
  Brookside Street – 2.9%
  Navajo Street – 8.9%
  Ramona Avenue – 6.5%
  St Elmo Avenue – 2.4%

## Slide 10
Eastbound Ramp
  Single eastbound right on to Tejon
  Two eastbound through lanes with dual right turn lanes at Nevada
Proposed Improvements
Tejon
Nevada
Notes: Provides mobility options for short trips
  Reduces vehicle trips by cars and ride share services
  Reduces congestion
  Complements transit service

## Slide 11
Eastbound Ramp Intersections
Proposed Improvements
Tejon
Nevada
Notes: Provides mobility options for short trips
  Reduces vehicle trips by cars and ride share services
  Reduces congestion
  Complements transit service

## Slide 12
Nevada Avenue
  Northbound Nevada reconfigured to allow both left and middle lanes to access northbound I-25
  Install median between the ramps and Brookside
Proposed Improvements
N
Notes: Provides mobility options for short trips
  Reduces vehicle trips by cars and ride share services
  Reduces congestion
  Complements transit service

## Slide 13
Motor Way
  Two-lanes with bike lanes
  Right-in/right-out at Nevada, remove signal
Proposed Improvements
Tejon
Nevada
Notes: Provides mobility options for short trips
  Reduces vehicle trips by cars and ride share services
  Reduces congestion
  Complements transit service

## Slide 14
Motor Way Intersections
Proposed Improvements
Tejon
Nevada
Notes: Provides mobility options for short trips
  Reduces vehicle trips by cars and ride share services
  Reduces congestion
  Complements transit service

## Slide 15
Brookside Avenue
  Fix intersection offset at Nevada
Proposed Improvements
Notes: Provides mobility options for short trips
  Reduces vehicle trips by cars and ride share services
  Reduces congestion
  Complements transit service

## Slide 16
Pedestrian/Bike
  Wider sidewalks
  Install additional sidewalks
  Narrow pedestrian crossings at Nevada/Motor City
  Bike lanes on Motor City
  Green painted bike crossings on Tejon
  Protected bike lanes at Tejon/Motor City
Proposed Improvements
Notes: Provides mobility options for short trips
  Reduces vehicle trips by cars and ride share services
  Reduces congestion
  Complements transit service

## Slide 17
Roadway
  Pavement Overlap south from Brookside
  Upgrades to sidewalks and pedestrian ramps at intersections
Rebuilt Traffic Signals
  St. Elmo
  Ramona
  At Chick-Fil-A access
CDOT Planned Improvements
Notes: Provides mobility options for short trips
  Reduces vehicle trips by cars and ride share services
  Reduces congestion
  Complements transit service

## Slide 18
Traffic Redistribution

## Slide 19: QUESTIONS?